## Slide 1: Belief-Rewards to Learn Radar Scheduling Policies
Amos Hebb
Raviraj S Adve
Zhen Qu
Zhen Ding

## Slide 2: Forecast
A radar scheduler’s goal is to sequence beams to best understand its environment.
Belief-dependent rewards can be used to develop both search and tracking policies.

## Slide 3: Outline
Introduction
Background
System Model
Implementation
POMDP
Solvers
Numerical Results
Summary

## Slide 4: Motivation
Beam-agile radars can select beams in any order
Goal is to best understand environment
Existing approaches:
  Treat Search and Track as independent functions
  Independently reduce resource usage
  Meet operator or system designer “requirement”
  Collaborate by a scheduler, dropping or shifting tasks
  Fragile performance in changing environments

## Slide 5: Problem Statement
Beam-Agile sensor is controlled by an agent
Agent select’s beam direction
Goal: understand the environment
Formulate Problem as a POMDP
Within framework:
  belief: set of particle filters
  solver: with belief-reality distance oracle, make policy
  policy: use belief to select next beam

## Slide 6: System Model: POMDP
S state space A action space T transition R reward space
O observation space Z observation probability ρ belief reward u belief updater

## Slide 7: System Model: Radar
Like closed-loop system in BWW[1]
Surveillance region polar coordinates from – π to π
Sensor at origin
Fixed beam width: π/15 rad
Range: 20km to 200km
pdetection: SNR such that pdetection = 0.5 at 100km
dwell time: 0.2s
targets piecewise-constant velocity from 0 to 700 m/s
[1] M. Byrne, K. White and J. Williams, "Scheduling multifunction radar for search and tracking," 2015 18th ISIF (FUSION), pp. 945-952.

## Slide 8: Implementation: POMDP
State Space, [(x,y,x',y'),…]
Action Space, [0,1)
Transition Function, apply x' to x
Observation Function
  Select visible, in range, targets
  Filter targets by comparing Pd to random number
  Convert to theta and radial velocity
  Add gaussian noise
  Include target id

## Slide 9: Implementation: BMDP
Updater
  Set of particle filters
  Observations initialize and update
BMDP
  Solve like MDP
  Belief state – result of applying updater
    Particle Filters as basic trackers
    Vector of action recency as history
  ρ(s, b) can be defined as r(s, a)

## Slide 10: Implementation: Baseline Solvers
Random Solver: Emits random policy
Sequential Solver: Emits beam sweep policy
Single Sweep Solver: Rotates once then stops
Highest Variance Solver: Emits heuristic policy

## Slide 11: Implementation: Learned Solver
Belief-BetaZero Solver:
  Progressive widening for continuous state, action
  BetaZero based on AlphaZero for POMDPs
  Modified BetaZero solver for ρPOMDP with no r(s,a).
  Offline component, collects data, trains prediction model, iteratively improves prediction model.
  Emits a policy which uses learned estimator to execute online Monte Carlo Tree Search

## Slide 12: Results
Expected Belief-Reward

## Slide 13: Results
Understanding Belief-Reward
Single Sweep Policy – Single Target – Single Detection

## Slide 14: Results
Understanding Belief-Reward
Sequential Policy - Single Target

## Slide 15: Results
Understanding Belief-Reward
Sequential Policy - Many Targets

## Slide 16: Results
Understanding Belief-Reward
Heuristic Policy - Many Targets

## Slide 17: Results
Understanding Belief-Reward
Learned Policy

## Slide 18: Results
1000 runs, 1-20 targets

## Slide 19: Results
Learned Policy Makes Non-Highest Variance Decision

## Slide 20: Summary
Training a policy solely focused on enhancing a belief model shows improvements over a random selector.
Policies are decoupled from the environment and belief dimensionality.

## Slide 21: Questions?
a.hebb@mail.utoronto.ca